## Slide 1
Special features of cantera-avbp

## Slide 2
Several features are coded in cantera-avbp
AVBP transport model
The use of custom kinetics
Thickening a flame
Alternative remeshing possible
Partial Equilibrium Assumption for 2S chemistry
Flamelet computation
Soot equations
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 3: 1.Transport
What are we talking about ?
: Diffusion coefficient [m2/s]
: Thermal conductivity [J/K/m3]
: dynamic viscosity [Pa.s]
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 4: 1.Transport
: the mass of species k
: the collision diameter of species k
T : temperature of the mixture
: collision integral
https://www.cerfacs.fr/avbp7x/HELP/MOULINETTE/XML2AV/xml2av.pdf
You have anyway in cantera, based on Lennard-Jones potentials :
- For the viscosity :
- For the heat conductivity :
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 5: 1.Transport
p : pressure
: reduced molecular mass
: the collision diameter of species k
T : temperature of the mixture
: collision integral
- For the diffusion :
Inverse a diffusion matrix to each coefficient .
✅ Best in terms of accuracy.
❌ Very very long !!
✅ Best in terms of accuracy/cost.
❌ Still costly if used in 3D codes.
1. Multi
2. Mix
gas.transport_model = ‘Multi’
gas.transport_model = ‘Mix’
transport = ‘Multi’
Or
in the .cti
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 6: 1.Transport
3. Lewis ( 1)
Simplified expression
✅ Very low cost.
❌ Big loss in accuracy !
gas.transport_model = ‘UnityLewis’
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 7: 1.Transport
4. AVBP ()
✅ Low cost.
❌ Loss in accuracy, you have to check !
Power law
Sutherland law
or
Simplified expression from
Simplified expression from
gas.transport_model = ‘AVBP’
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 8: 1.Transport
Gri 30 with T=300K, P=1bar.
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 9: 2. Customkinetics
If you want to give another thing to CANTERA than the information provided in a .cti.
A f90 to be included in the code
Useful if you want to have a special handling of the kinetics (ex: algebraic relations between species)
kinetics = ‘custom’
in the .cti
in the script
import cantera as ct
ct.compile_fortran(‘mechanism.f90’)
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 10: 3. Thickening
To be able to test the chemistry for
https://cerfacs.fr/chemistry-repo/pub/cantera_jypnb/Thickening.html
f.flame.thick = value
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 11: 4. Alternative remeshing
Three options for “refine_grid” parameter:
“disabled” : no refinement. Can be useful if one wants to test a regular-spaced grid.
“refine” : default refinement method of CANTERA. Is very useful to refine more the flamefront than the edges.
“remesh” : CERFACS method, useful to go from one grid to another.
refine_grid = ‘remesh’
f.solve(loglevel, refine_grid)
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 12: 5. Partial Equilibrium Assumption (PEA)
Special to BFER -> correction for the rich part.
Only available with AVBP format.
https://cerfacs.fr/chemistry-repo/pub/cantera_jypnb/Pea.html
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 13: 6. Flamelet computation
Mixture fraction variable : z
https://cerfacs.fr/chemistry-repo/pub/cantera_jypnb/CDF-Flamelet.html
Trick : change of space from
x (position) to z (mixture fraction)
✅ Faster computations (20s instead of 200s).
✅ Better stability (CDF is very capricious.
❌ No return possible to x-space.
f = ct.Flamelet()
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 14: 7. Soot equation
Enables the computation of soot after a flame in cantera
https://cerfacs.fr/chemistry-repo/priv/cantera_soot/Handbook_cantera-soot.pdf
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 15: Bonus: Cantera as an input of AVBP
It is possible to generate a 1D flame from Cantera and make an initialization for AVBP
It is possible to generate a gas_out with the help of Cantera.
It is possible to use Cantera to calculate evaporation with evol_evap0D.
It is possible to create the mixture_database.dat with the xml2av tool.
f.write_AVBP(‘name_of_file.csv’)
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 16: Bonus 2: Cantera as an input of AVBP
You have a separate git called cantera-tools
  Initialize 3D AVBP calculations with cantera
  Optimize Schmidt & Prandtl numbers
https://chemistry.cerfacs.fr/en/avbp/avbp-tools-for-chemistry/
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..

## Slide 17: BACKUP
https://chemistry.cerfacs.fr/en/cantera/cantera-tutorials/
http://www.cmap.polytechnique.fr/~giovangi/convergent.pdf
Notes: ----- Notes de la réunion (12/11/2014 12:11) -----
CA can perform 0D simulation so equ cal & time evol of closed and open reactors
It can also perform STEADY 1D simulations, mostly premixed configurations but a counterflow diffusion flame model is also implemented
recently it also became possible to add surface ..